## Slide 1: Seeing at Dome A, Antarctica: automatic measurements & results
Bin MA
(NAOC)
2020-11-26 @ Xiamen

## Slide 2: outline
1 Introduction
2 KL-DIMM for Dome A
3 Operations of KL-DIMM
4 Seeing results from Dome A
5 Summary

## Slide 3: 1 Introduction
Seeing: a key parameter in site-testing
The best mid-latitude sites: 0.6 – 0.8”
Turbulence in the atmosphere
  Boundary layer (BL)
  Free atmosphere
Antarcitca: thin BL
Dome C:
  BL thickness ~ 30 m
  seeing obove BL ~ 0.3”
boundary layer
free atmosphere
Marks+1999
britastro.org
good <== seeing ==> bad

## Slide 4: Dome A (Kunlun Station)
the highest point (4093 m) in Antarctic plateau
  BL thickness ~ 14 m by Snodar
  yet only daytime seeing: median 0.8” @ 3 m by DIMM (Differential Image Motion Monitor)
credit: Dome C group
Pei+2013
Bonner+2010
Dome A C

## Slide 5: night-time seeing @ Dome A?
Challenges
  Unattended for almost a year
  Low temperature
  Limited power supply & network
  Small FoV of DIMM
  A tower for DIMM
Hu+2019

## Slide 6: 2 KL-DIMM for Dome A
KL-DIMM: the automatic DIMM for KunLun station (ambient -80℃)
  Active thermal control for electronics
  Mechanical improvement
  two KL-DIMMs for redundancy
Tower: 8 m designed by TJU
  Logistical limit
  BL < 9 m for 25% time

## Slide 7
cold tests: single-part/whole system
  working/rebooting correctly at -70C
  ~100W including heaters
test obs @ Muztagh Ata: seeing precision ~ 10%
low temperature chamber @ NIAOT

## Slide 8
2 KL-DIMMs were installed at Dome A in 2019
2 members from NAOC + help from another 2 astronomers + the traverse team
supported by PLATO-A

## Slide 9: 3 Operations of KL-DIMM
in-situ work
  installation
  rough polar alignment
  searching the target
fully automatic observation
data processing in real-time
seeing results were sent back every 30 min, and shown in website

## Slide 10: software system
experience from Antarctic Survey Telescopes (AST3)
hardware control
  telecope, camera, heaters, sensors ...
observation flow:
  pointing correction
  imaging & close-loop tracking
  short-exposure sequence
  real-time data analysis
  transfering results to Beijing
polar misalignment:
<0.3 deg in left-right
<0.1 deg vertically

## Slide 11
KL-DIMM2 functioned well, while KL-DIMM1 had some issues
special issue at Dome A: de-icing by ITO heating
first DIMM operations in the winter at Dome A
7 x 24 hr operation
working well even T < -75℃

## Slide 12: 4 Seeing results from Dome A
April - Aug 2019
histogram of night-time seeing: a sharp peak (<0.5”) + a long tail (up to >3”)
log-normal distribution in mid-latitude sites
2 or 3 log-normal components in Antarctica
Muztagh Ata
Xu+2020
Dome A
Ma+2020
Dome C
Aristidi+2009

## Slide 13
the 3 components in the histogram: FA, BL & intermediate seeing
caused by the variation of BL thickness
at just 8 m, FA seeing was obtained for 31% of the time, when the median was 0.31”
Snodar: BL < 9 m for 25% time
FA ~ 0.3”
8 m
boundary layer
---> time
Seeing (”)
Number
Ma+2020

## Slide 14
the seeing could be improved on a higher tower: more FA seeing, smaller BL seeing
Dome A, 8 m
Ma+2020
Dome C
Aristidi+2009

## Slide 15
KLAWS: weather data on multi-heights between 0 - 14 m
simultaneous operations: Jan - March
larger temp gradient => thinner BL
winter data in 2015: 50% time when hBL<14 m
Ma+2020

## Slide 16: 5 Summary
KL-DIMM: successful operations @ Dome A
  -75℃ & fully automatic
  could be used for other sites
direct measurements prove the superb seeing @ Dome A
with many other advantages (Shang 2020 RAA), Dome A is potentially the best optical/IR/THz site on the earth

## Slide 17: Thank you！
acknowledgement
the Chinese Antarctic expedition team
Dr Z. Li, F. Du, Z. Hu, T. Song, E. Aristidi and K. Agabi